## Slide 1: Applications of Autonomous Drones for Non-Terrestrial Networks in Remote Areas
By: Andrés Navarro Pedregal
Tutor: José Alberto Hernandez Gutiérrez

## Slide 2: Table of contents 01 05 04 02 06 03
Introduction & Objectives
Building the System
Flight Tests
Technical Details
Conclusions
Building the Drone

## Slide 3: Introduction & Objectives 01

## Slide 4: Project & Objectives
Study of UAVs for NTNs applications
Develop BOM, manual of design, etc
Human rescue tasks with ML and VR goggles
Viability of UAVs for NTNs
Create a budget UAV for research
Application of UAVs for remote areas

## Slide 5: Technical Details 02

## Slide 6: Flight performance
Weight: 6.5KG
Range: Up to 40Km
Flight time: 25-35 minutes
Autopilot capabilities
Retractable landing gear

## Slide 7: Main components
Frame | Tarot X690 | 17 inch propellers
Motors | T Motor U7 490kv | Up to 3kg per motor
Esc | TMotor Flame 70A LV | 
Flight controller | Pixhawk 6c | Using Ardupilot
GPS | Holybro M9N | 1.5m CEP precision
Battery | Tattu 4s 22Ah | 
Radio link | RFD868x | With mavlink telemetry
Controller | Radiomaster TX16S MAX | 
Price: 2600€

## Slide 8: 5G NTN Components
Onboard Computer | Jetson Orin Nano | 8GB RAM 5.3 FP32 TFLOPs
360 camera | Ricoh Theta X | 4K 30fps usb stream
4G/5G router | (GL-X750V2) Smart WiFi | Dual band, OpenWrt
Price: 1800€

## Slide 9: Building the Drone 03
Detail of the drone built: arXiv:2409.19337

## Slide 10: Drone Architecture
360 Camera
Onboard
computer
5G Router
PDB
ESC
Motors
Flight Controller
Battery
GPS
Telemetry Control

## Slide 11: Component placement

## Slide 12: Component placement

## Slide 13: 3D printed parts

## Slide 14: 3D printed parts

## Slide 15: Build Complete!

## Slide 16: Building the System 04

## Slide 17: Steps
💻 Edge Computing
🧍 Detect People
🚨 Monitor Alerts
🥽 VR Integration

## Slide 18: High Level Overview
Drone
Server
☁️
VR Goggles
Experiments with Meta Quest 3: 10.1109/ICTON62926.2024.10647326

## Slide 19: Architecture
📷
360 camera
💻
Object Detection
🔍
Object Detection
🚨
Alert
🌐
Drone
Server
VPN Tunnel
🧠
LLM Integration

## Slide 20: Drone
Edge Computer with GPU
360 Camera
Router

## Slide 21: Server

## Slide 22: DB Schema
🚁
🗺️
🚁
🚁
Drone
📸
Detection
🟰
Rules
🚨
Alert
🗺️
Mission
🧍
User

## Slide 23: Live Connection of the Camera

## Slide 24: Flight Tests 05

## Slide 25: Detection Tests

## Slide 26: Detection Tests

## Slide 27: LLM functionality

## Slide 29: Random Detections

## Slide 30: Flight Time: 30min Detect Anything Real Time Video Tx
Even the drone itself!

## Slide 31
Presented in the Science for Industry (S4I) Conference

## Slide 32: Thank you!
Any questions?