## Slide 1: Applications of Autonomous Drones for Non-Terrestrial Networks in Remote Areas
By: Andrés Navarro Pedregal
Tutor: José Alberto Hernandez Gutiérrez
March 11, 2025. Leganés, Madrid, Spain
Dual Bachelor in Data Science and Engineering and Telecommunication Technologies Engineering

## Slide 2: Table of contents 01 05 04 02 06 03
Introduction & Objectives
Building the System
Flight Tests
Technical Details
Conclusions
Building the Drone
Andres Navarro Pedregal

## Slide 3: Project
Create a UAV for NTN applications
Part of a research project from the Telematics Department @ UC3M funded by the 6G Integration 3
Andres Navarro Pedregal
Research different applications UAVs

## Slide 4: Objectives
Build a budget and modular UAV for research
Adaptable to different research purposes for NTNs
Propose multiple use-cases (e.g. human rescue)
Andres Navarro Pedregal

## Slide 5: Characteristics
Weight: 6.5KG
Range: Up to 40Km
Flight time: 25-35 minutes
Autopilot capabilities
Retractable landing gear
ML & AI Intelligence Integrated
Andres Navarro Pedregal

## Slide 6: Drone Architecture
360 Camera
Onboard
computer
5G Router
PDB
ESC
Motors
Flight Controller
Battery
GPS
Telemetry Control
Andres Navarro Pedregal

## Slide 7: Main components
Frame | Tarot X690 | 17 inch propellers
Motors | T Motor U7 490kv | Up to 3kg per motor
Esc | TMotor Flame 70A LV | 
Flight controller | Pixhawk 6c | Using Ardupilot
GPS | Holybro M9N | 1.5m CEP precision
Battery | Tattu 4s 22Ah | 
Radio link | RFD868x | With mavlink telemetry
Controller | Radiomaster TX16S MAX | 
Andres Navarro Pedregal
2599 €
Notes: poner precios

## Slide 8: Components
Andres Navarro Pedregal

## Slide 9: Components
Andres Navarro Pedregal

## Slide 10: Full Build
Andres Navarro Pedregal

## Slide 11: High Level Overview
Drone
Server & Ground Station
LLMs
Andres Navarro Pedregal

## Slide 12: 5G NTN Components
Onboard Computer | Jetson Orin Nano | 8GB RAM 5.3 TFLOPs
360 camera | Ricoh Theta X | 4K 30fps USB livestream
4G/5G router | (GL-X750V2) Smart WiFi | Dual band, OpenWrt
Andres Navarro Pedregal
1804 €
Notes: footer uc3m, andres navarro marzo 2025

## Slide 13: Architecture
📷
360 camera
💻
Object Detection
🔍
Object Detection
🚨
Alert
🌐
Drone
Server
VPN Tunnel
🤖
LLM Integration
Andres Navarro Pedregal

## Slide 14: Drone
Edge Computer with GPU
360 Camera
Router
Andres Navarro Pedregal

## Slide 15: Server
Andres Navarro Pedregal

## Slide 16: DB Schema
🚁
🗺️
🚁
🚁
Drone
📸
Detection
🟰
Rules
🚨
Alert
🗺️
Mission
🧍
User
Andres Navarro Pedregal

## Slide 17: Open Source Code
Code can be found in: https://github.com/orgs/6G-Integration-3-UC3M/repositories
Andres Navarro Pedregal

## Slide 18: Live Connection of the Camera
Andres Navarro Pedregal

## Slide 19: Detection Tests
Andres Navarro Pedregal

## Slide 20: Detection Tests
Andres Navarro Pedregal

## Slide 21: LLM functionality
Andres Navarro Pedregal

## Slide 22
Andres Navarro Pedregal

## Slide 23: Random Detections

## Slide 24: Videos
https://www.youtube.com/watch?v=IqNsVOT3uFQ
https://www.youtube.com/watch?v=kdMgwRRte-8
Andres Navarro Pedregal

## Slide 25: Flight Time: 30min Detect Humans Autonomously Real Time Video Transmission
Andres Navarro Pedregal

## Slide 26: Showcase
Science for Industry (S4I) Conference
6G Integration 3
Part of a Paper
https://arxiv.org/abs/2409.19337
Andres Navarro Pedregal
Notes: JCR

## Slide 27: Thank you!
Any questions?